VuPoint Soulutions: Magic Wand Quick Set Up Guide

Turn on and off the device:

Press and hold the silver scan button on the top of the scanner for two to three seconds until the display turns on. Press it again for two to three seconds when you wish to turn off the scanner.

Note: If the display doesn’t turn on, please replace the two “AA” batteries by sliding back the cover on the top.

Scan a document:

Align the scanner with the page or item you want to scan. Make sure the scanner is turned on. Press and release the scan button, the green scan light should now be lit (if not, see note above). With a slow steady motion glide the scanner along the document you are scanning, once you stop moving the scanner it will automatically stop scanning. The green scan light should now be off. The number on the screen should have just increased by one number indicating it completed the scan. The number indicates how many images are currently stored on the memory chip. Repeat this process for all the other scans you wish to do. Press and hold the scan button for two to three seconds to turn the scanner off when you’re done scanning.

Tip: you will notice two white arrows on the front and back of the scanner. This is the area that will get captured in the scan.

Upload images to a PC:

Connect the USB cable included in the box to the front of the scanner. Connect the other end to the PC you want to upload to. Turn on the scanner by pressing the scan button for two to three seconds. The scan wizard should appear and you can follow the on screen instructions for transferring the images. You can also navigate to the device using Windows Explorer and drag and drop the images to the folder you want them in.

Format the micro SD card when you are finished uploading to the PC to ensure your privacy. Turn on the scanner, Press the FORMAT button with a straightened paper clip. You should see an “F” on the display. Press the SCAN button to start formatting the micro SD card. The micro SD card indicator will blink until the formatting process is complete.

Err Light:

If the red Err light appears while scanning stop scanning and try it again. I usually try to go a little slower and steadier and that clears up the error. Also check to see what the DPI is set to. If it set to “HI” it should take you about 12 seconds to scan a page. That setting is good for photos.

DPI:

Dots per inch. The three settings are “LO” for the lowest setting (default). “MI” for middle setting and “HI” for the highest setting. I usually keep it on “LO” unless I plan on scanning pictures.